## Slide 1: CPU organization / Main Memory

## Slide 2: Components of CPU
Control Unit:
Manages and coordinates the operations of all components of the computer.
Reads instructions, interprets them and generates signals for appropriate actions.
Arithmetic Logical Unit (ALU):
All calculations and comparison operations are performed in ALU.
Thus the actual processing of data takes place in ALU.

## Slide 3
During the processing of a job, data may move back and forth several times between primary storage (for intermediate results and other data) and ALU before processing of the job is over.
Almost all ALUs are designed to perform four basic arithmetic operations (add, subtract, multiply, and divide) and logical operations such as less than, greater than and equal to.

## Slide 4
Basic functional units of a computer
Primary Storage
Secondary Storage
Input Data
Output Data
Control Unit
ALU
Program
and data
Result
Storage unit
Central processing unit
Data Flow
CPU Control

## Slide 5: CPU Registers
As a CPU interprets and executes instructions, there is a movement of information between various units of the computer.
To handle this process, and to speed up the information transfer rate, the CPU uses some special memory units, called registers.
Registers hold information on a temporary basis and are part of CPU (not the main memory).
The length of a register is the number of bits it can store. Length of a register is sometimes also called its word-size.
Most CPUs these days have 32-bit or 64-bit registers.

## Slide 6
The number of registers varies from computer to computer. However, there are some registers common to all computers. These are described below:
Memory Address Register (MAR)
  It holds the address of the active memory location.
  It is loaded from the program control/counter register when the system reads an instruction from the memory.
Memory Buffer/Data Register (MBR) (or MDR)
  It holds the contents of the accessed memory word.
  The system transfers an instruction word placed in this register to instruction register.

## Slide 7
  A data word placed in this register is accessible for operation with accumulator register or for transfer to I/O register.
3. Program Control/Counter Register (PCR)
  It holds the contents of the next instruction for execution.
  Normally the instructions are executed in a sequential manner.
4. Accumulator Register (AC)
  It holds the data on which the system has to operate, intermediate results, and results of operations performed.
  The system returns the result of an arithmetic operation to accumulator register for transfer to main memory through MBR.

## Slide 8
5. Instruction Register (IR)
  It holds the current instruction under execution.
  As soon as the instruction is put in this register, its address and execution parts are separated. The address part is sent to MAR and the instruction part is sent to the control unit for getting decoded.
6. Input/Output Register (I/O)
  It is used to communicate with the input/output devices.
  All input/output information is transferred through this register.

## Slide 9: Memory
A computer’s CPU has necessary circuitry for data processing and controlling other components of the computer.
But is does not have place to store programs and data needed during data processing.
CPU has several registers for storing data and instructions, but they can store only a few bytes at a time, sufficient only to hold one or two instructions.
If the data is stored in the secondary storage, CPU will be idle most of the time, as there is a great mismatch between the CPU speed and the rate of transfer of data from the disk to the computer.
Therefore, every computer has a memory storage, called primary storage or main memory which reduces this mismatch significantly.

## Slide 10
Instructions and data of a program reside mainly in the main memory when CPU is executing the program.
Main memory of a computer consists of several small storage areas called locations or cells.
Each location can store a fixed number of bits called the word length (or word size) of the memory (usually 16, 32, or 64 bits).
Each location has a built in unique number assigned to it, called the address of the location.
……
0
1
2
…
bits
N-1

## Slide 11: System Bus
A computer stores in the memory the data and instructions of a program in execution, and fetches and loads them into CPU registers as the program execution proceeds.
Thus CPU and memory interact frequently. This interaction is facilitated by a bus.
A bus is a communication pathway connecting two or more devices of a computer.
Multiple devices connect to the bus, and a signal transmitted by any device is available for reception by all other devices attached to the bus.
Only one device at a time can successfully transmit a signal.

## Slide 12
A bus contains several separate lines, each is assigned a particular meaning or function.
The data lines provide a path for moving data between system modules. Collectively, these lines are called the data bus.
When people refer to the bus of a computer, they usually mean the data bus.
A data bus typically consists 8, 16, 32 or 64 separate lines. The number of such lines is called the width of the data bus.
The width of the data bus determines the how many bits can be transferred at a time, and it is a key factor in determining the system performance.
The address lines are used to designate the source or destination of the data on the data bus. Together, the address lines are called the address bus.

## Slide 13
The control lines are used to control use of the data and address lines. The control lines together are called the control bus. The control bus carries the signals to read or write the data to a specified address location.
Thus in a memory access by the CPU, control bus carries memory access command, address bus carries memory address, and data bus carries the data.

## Slide 14
CPU
Main Memory
Data Bus
Control Bus
Address Bus
Buses between CPU and Memory

## Slide 15
Instruction Decoder
R(n-1)
R0
A B
ALU
MAR
MDR
PC
IR
Y
Z
Add
Sub
ALU Control Lines
MEMORY
Address
Lines
Data
Lines
Single-bus organization of the Data paths inside the CPU
Internal Bus